## Slide 1
MAE 224
Lab 2 Velocity and Pressure
2021.2.22

## Slide 2
Lab2 Objectives
Understand the principles of pitot tube
Application of Bernoulli’s Equation
Measure air velocity
Other velocity measurements
Pitot Tube Built by Mike Vocaturo
Anemometer
Goggle
Lab Kits

## Slide 3
Streamline
A streamline is a curve that is everywhere tangent to the instantaneous local velocity vector
Crowe and Elger, Fluid Mechanics
Parallel Streamlines
Converging Streamlines
More complicated streamlines over an airfoil section
Streamline Examples
Velocity
Acceleration
s: 1D streamline coordinate
t: time
et: unit vector for tangential direction
Acceleration (by chain rule)
Notes: Use curvilinear coord.
For a certain streamline, s is the 1D streamline coordinate to describe the position on that streamline.
t is time.
e_t describes the unit directional vector tangential to the streamline, and by definition, it also represents the local velocity direction.
So the velocity field can be expressed in this way.

## Slide 4
Euler’s Equation
Pressure force 1
Pressure force 2
Gravity
Consider a small cylindrical element oriented in arbitrary direction l
Force analysis only along l direction
Assume no viscous forces (inviscid)
Cross section
Notes: viscous force is like the friction force exerted on the cylindrical element due to the fluid motion.

## Slide 5
Euler’s Equation
Force analysis only along l direction: apply Newton’s 2nd law
Valid only for inviscid, incompressible (ρ constant) flow

## Slide 6
Bernoulli’s Equation
Start from Euler’s
arbitrary direction l
Velocity flow field along one streamline
Acceleration field
Choose l to be the tangential direction of the streamline et
Velocity
Acceleration
Assume steady
const along a streamline
Inviscid, incompressible, steady flow

## Slide 7
Bernoulli’s Equation
1
2
3
Along one streamline
Inviscid, incompressible, steady flow
What about point 3, or across streamlines?
Bernoulli’s Equation can be applied across streamlines only for irrotational flows (Smits, Ch6)
Vorticity
irrotational
rotational
How does tiny fluid element move with the flow?
???

## Slide 8
Pitot Tube and Bernoulli’s Equation
Velocity @ stagnation point V2= 0
z1 = z2
Total Pressure
(Stagnation Pres.)
Static Pressure
Dynamic Pressure
Stagnation point
V = 0
The one in our lab kits
How to measure the pressure?
Manometer!

## Slide 9
U-tube Manometer: pressure measurement
Hydrostatic equations
Bernoulli’s equation (along the same streamline)
Combined together
A. Smits, A Physical Introduction to Fluid Mechanics
Stagnation point
Detailed Example (P85)
Liquid
Notes: Cannot neglect that term if you are measuring the liquid velocity instead of air velocity, (putting pitot tube in another liquid)

## Slide 10
Manometer: pressure measurement
Pitot Tube Built by Mike Vocaturo
Air flow
Stagnation point
Open end
P0 = 1 atm
Connect to pitot tube
The stagnation point is at the tip of the small metal tube inside.

## Slide 11
Pitot Tube, Piezometer and Pitot Static Tube
Different tip designs
Total Pressure / Stagnation Pressure
Static Pressure
Combination: can measure total pressure and static pressure
=> Can directly determine the local flow velocity (Ptotal – Pstatic)
The one in our lab kits
Stagnation point

## Slide 12
Total pressure
Static pressure
Pitot Static Tube
Aircraft use pitot tubes to measure airspeed.
Airflow
Airbus A380
Stagnation point
Kamov Ka-26 helicopter
Pitot tubes on
Boeing 777
https://en.wikipedia.org/wiki/Pitot_tube

## Slide 13
Pitot Static Tube
https://en.wikipedia.org/wiki/Pitot_tube
Formula one

## Slide 14
Other velocity measurements
Vane and cup anemometer
Hot-wire anemometer
Particle Image Velocimetry
Phase Doppler Anemometry

## Slide 15
Other velocity measurements
Vane and cup anemometer is used to measure wind speed or water speeds.
Vane and cup anemometer: the speed of rotation is proportional to flow speed

## Slide 16
Other velocity measurements
Hot-wire anemometer
Flow causes hot wire to cool down as a result of convection;
Resistance of hot wire changes, causing voltage also to change;
Measure voltage change to calculate flow velocity.
Good for measuring velocity fluctuations in turbulent flows
Small sensing element reduces disturbance to surrounding flow

## Slide 17
Other velocity measurements
Particle Image Velocimetry (PIV): full-field, non-intrusive
  Seed tiny particles (1-10 um) in the flow that completely follow fluid motion
  Illuminate particles with a laser sheet parallel to velocity field of interest
  Camera records two images of particles at two laser pulses
  Calculate the particle displacement between two images.
  Velocity = displacement/Δt

## Slide 18
Other velocity measurements
Particle Image Velocimetry (PIV): full-field, non-intrusive
Flow Motion

## Slide 19
Other velocity measurements
Phase Doppler Anemometry (PDA): non-intrusive, high accuracy
Probe volume is small, but can be compensated by scanning the whole flow field
  Also need to seed tiny particles
  Light is scattered from particles, which contains a doppler frequency shift proportional to particle velocity
  Velocity can be calculated by the frequency of the interference pattern collected by the photo-detector

## Slide 20
Any Questions?

## Slide 22
Lagrangian and Eulerian Flow Descriptions
Lagrangian: follow individual fluid particle and determine how the fluid properties change with time.
Eulerian: fluid properties at fixed points, as functions of both space and time.
Example of smoke discharging from chimney
Lagrangian: follow particle A, and measure its temperature only, TA = TA (t)
Eulerian: measure temperature at different points (x,y)
Temperature field T = T (x,y,t)
Similarly, velocity field…
Donald F. Young
A Brief Introduction to Fluid Mechanics
Notes: To understand the principles of pitot tube, we should start from the basic concepts in fluid kinematics.
Eulerian is usually the easier way to describe a flow.

## Slide 23
3D Velocity field
Donald F. Young
A Brief Introduction to Fluid Mechanics
All three components depend on space (x, y, z) and time (t)
How to express acceleration for a fluid particle?
Along the particle path, VA is a function of space and time
Position is also a function of time!
By definition of acceleration and chain rule
3D Acceleration field!
Notes: With the eulerian flow description,